## Slide 1: Swarm Robotics Workshop
Dr. Andrew Vardy
Bio-inspired Robotics (BOTS) Lab
Department of Computer Science
Department of Electrical and Computer Engineering
Memorial University of Newfoundland
St. John’s, Canada

## Slide 2: Where I’m from
St. John’s, Canada

## Slide 3: Swarm Robotics?
“Swarm robotics is the study of how a large number of relatively simple physically embodied agents can be designed such that a desired collective behavior emerges from the local interactions among the agents and between the agents and the environment.”
  [Şahin, E. (2004). Swarm robotics: From sources of inspiration to domains of application. In International workshop on swarm robotics (pp. 10-20). Springer, Berlin, Heidelberg.]

## Slide 4
“Swarm robotics is the study of how a large number of relatively simple physically embodied agents can be designed such that a desired collective behavior emerges from the local interactions among the agents and between the agents and the environment.”

## Slide 5
“Swarm robotics is the study of how a large number of relatively simple physically embodied agents can be designed such that a desired collective behavior emerges from the local interactions among the agents and between the agents and the environment.”

## Slide 6
“Swarm robotics is the study of how a large number of relatively simple physically embodied agents can be designed such that a desired collective behavior emerges from the local interactions among the agents and between the agents and the environment.”
robots

## Slide 7
“Swarm robotics is the study of how a large number of relatively simple physically embodied agents can be designed such that a desired collective behavior emerges from the local interactions among the agents and between the agents and the environment.”
Kilobots: 1024
S-bots: 10-20
Fewer, more capable robots
Many
limited
robots
robots

## Slide 8
“Swarm robotics is the study of how a large number of relatively simple physically embodied agents can be designed such that a desired collective behavior emerges from the local interactions among the agents and between the agents and the environment.”

## Slide 9
“Swarm robotics is the study of how a large number of relatively simple physically embodied agents can be designed such that a desired collective behavior emerges from the local interactions among the agents and between the agents and the environment.”
Direct communication (local)
Indirect communication (perceive results of others actions)

## Slide 10: Characteristics of Swarm Robotics
Swarm Robotics: A multi-robot system with the following characteristics:
  robots are autonomous;
  robots are situated in the environment and can act to modify it
  robots’ sensing and communication capabilities are local
  robots do not have access to centralized control and/or to global knowledge
  robots cooperate to tackle a given task
Brambilla, M., Ferrante, E., Birattari, M., & Dorigo, M. (2013). Swarm robotics: a review from the swarm engineering perspective. Swarm Intelligence, 7(1), 1-41.

## Slide 11
  robots are autonomous;
  robots are situated in the environment and can act to modify it
  robots’ sensing and communication capabilities are local
  robots do not have access to centralized control and/or to global knowledge
  robots cooperate to tackle a given task
X
X
X
X
X
X

## Slide 12
Definition:
  “Swarm robotics is the study of how a large number of relatively simple physically embodied agents can be designed such that a desired collective behavior emerges from the local interactions among the agents and between the agents and the environment.”
Characteristics:
  robots are autonomous;
  robots are situated in the environment and can act to modify it
  robots’ sensing and communication capabilities are local
  robots do not have access to centralized control and/or to global knowledge
  robots cooperate to tackle a given task
What robots exist that adhere to this definition and exhibit these characteristics?

## Slide 13: Natural Robots: The Honeybees
Democratic nest selection
  Seeley, T. D. (2010). Honeybee democracy. Princeton University Press.
Waggle dance communication

## Slide 14: NATURAL ROBOTS: THE ANTS
Extremely successful family
  15 - 20% of terrestrial biomass
Leafcutter ants
  Invented agriculture millions of years before us!

## Slide 15: Natural Robots: The termites
Termite mounds taller than a computer scientist
  Construct extremely sophisticated structures…

## Slide 16
Sophisticated architecture and engineering from insects with small brains, poor vision, and no central coordination

## Slide 17: SELF-ORGANIZATION
“Self-organization is a set of dynamical mechanisms whereby structures appear at the global level of a system from interactions among its lower-level components. ”
  Bonabeau, E., Dorigo, M., & Theraulaz, G. (1999). Swarm intelligence: from natural to artificial systems
Individual ants, bees, termites, and robots interact locally… yet a global pattern emerges
  THE CENTRAL MYSTERY!

## Slide 18: Our tools: Blockly and Waggle

## Slide 19: waggle
We will be using Waggle, an online simulation and programming environment
  2-D Physics: Matter.js
  Visual programming: Blockly
There are other tools for simulating swarms of robots:
  Agent-based simulators: Netlogo, MASON
  Robot simulators: ARGoS, V-REP, Gazebo
Why another simulation tool?

## Slide 20
Easy to Use
Realistic
Netlogo
Waggle
V-REP
Gazebo
ARGoS
MASON
Abstract
Flexible

## Slide 21: Blockly
A library for building visual programming apps
  Started by Google, now open-source
  Used for hundreds of educational apps on the web and on Android / iOS devices
Programming for kids?
  Yes
  ”But we’re not kids”
  Blockly is an easily learned language for people with various levels of programming experience

## Slide 22: Exercise #1: Blockly Games 20 minutes
Go to Blockly Games:
  https://blockly-games.appspot.com/
Complete “Puzzle”
Complete as many levels as you can of “Maze”
Experienced programmers:
  There are interesting challenges as you progress into the higher levels

## Slide 23: Robotics Concepts

## Slide 24: The SENSE / ACT Cycle
Robots exist in a constant cycle of perception (via sensors) and movement (via actuators)
Robot
Sense
World
Act
Sensors
Actuators

## Slide 25
The robot’s controller may be very deliberative
  Carefully build a model of the world, plan a trajectory, then execute it
Sense
World
Act
Sensors
Actuators
Sense
Model
Plan
Act

## Slide 26
Or the controller may be reactive
  There is a direct mapping of sensor states to actions
  The model (if any) is small
Sense
World
Act
Sensors
Actuators
Sense
Act
We will be using
reactive controllers

## Slide 27: Tutorial Level

## Slide 28: The waggle PAGE
Go to the main Waggle page:
  http://bots.cs.mun.ca/waggle/
  Note that these slides are available here
Select the Tutorial level
Take note of the following features…

## Slide 29
Robot (try click and drag)
Blockly area
Robot-specific Blockly categories
}
Simulation area

## Slide 30
Within the Blockly area, click on the “Actions” category
Now click-and-drag on “Set speeds” and pull it into the open white area
Click on the ‘0’ next to “forward” and change it to some number in the range [-10, 10]
  Robot does not move
Click-and-drag “Execute” beneath “Set speeds” so that they connect like this:
  Now the robot moves!

## Slide 31: Our first controller!
So this is our first controller:
A controller senses the world, then acts
  But this controller is so basic, it doesn’t even do any sensing
The controller is executed by the simulator many times per second
  There is no need for a “loop”, the controller gets called over-and-over by default

## Slide 32: Our first controller!
So this is our first controller:
A controller senses the world, then acts
  But this controller is so basic, it doesn’t even do any sensing
The controller is executed by the simulator many times per second
  There is no need for a “loop”, the controller gets called over-and-over by default

## Slide 33: Deferred Execution
Notice how the robot did not move without “Execute”
  The controller uses a deferred execution model, meaning that nothing happens until “Execute”. The controller is executed top-to-bottom and each block in the “Actions” category sets something about the action the robot will take. However, no action is taken until “Execute”.
e.g. The following controllers all behave the same because the speeds set by the blocks on the bottom overwrite the speeds set above:

## Slide 34: Exercise #2: BASIC MOVEMENT 5 minutes
Experiment with “Set speeds” to derive controllers that travel in...
  Straight lines
  Circles
Note the importance of
Experiment with positive / negative speeds
  Try the following:
    Counter-clockwise circle, moving forwards
    Counter-clockwise circle, moving backwards

## Slide 35: Exercise #2: Review
Move forward (speed 10):
Turn clockwise (speed 10):
  Set angular speed negative for counter-clockwise turns
Move in a tight clockwise circle:
  Reduce angular speed for a larger circle; Reduce forward speed for a smaller circle
Use negative values for backward motion and counter-clockwise turns

## Slide 36: The Conditional BLOCK
Under “Logic” select the conditional block:
Connected to the top part will be a condition block which must evaluate to True or False
  If the condition block is True, the block(s) within the “do” will execute
Click on the star to customize this block. Here are some possibilities:

## Slide 37: Conditional + SENSORS
Create an if – else if – else conditional block:
Select the “Sensors” category and drag in these two blocks:
Now under the “Actions” category drag in two of these:
Also under “Actions” drag in an

## Slide 38
Connect the blocks together like this:
Note that you have to customize the text for each “Set robot’s text” block
Drag the robot around, bumping into the walls to test it

## Slide 39: Exercise #3: OBSTACLE AVOIDANCE 5 minutes
Replace the blocks with blocks and adjust the speeds to achieve this:
  Note: Should still work when bouncing against walls on the right
Conditions:
Should work with any number of robots

## Slide 40: Exercise #3: Review
Your solution should look something like this:
You could reduce the speeds a little, but the robot might hit the wall (not a big problem)

## Slide 41: WAGGLE: TOUR OF FEATURES AND BLOCKS

## Slide 42: Waggle Feature / Block Tour
Continuing on the Tutorial level, we will introduce some further features of the waggle page...

## Slide 43
Try adding more robots with
this slider

## Slide 44
Try adjusting this slider to see the simulation run in slow-motion
NOTE: Adjusting “Timescale” breaks up movement into smaller increments; This changes the sim’s behaviour and is therefore not exactly the same as “slowing time”.

## Slide 45
Use these buttons to save and load your controller.
When saving, the file saved will be set in this box
and it will always be saved into your Downloads folder.
Save your controllers throughout the workshop and give them sensible names. If you hit the browser’s refresh button, the current controller will be lost!

## Slide 46: Waggle Feature / Block Tour
Our next major topic is Object Clustering
Prior to introducing the swarm robotics perspective on this, we will take a tour through the features and blocks needed for clustering
Go to the main Waggle page (or just hit your browser’s back button):
  http://bots.cs.mun.ca/waggle/
Select the Pre-clustering level

## Slide 47
Adjust the number of pucks with this slider. You must hit the “Reset” button for the change to take effect.

## Slide 48: Sensors
Sensors are attached to the robot in different configurations; Here is the configuration we will focus on for now:
Note that the obstacle sensors cannot sense pucks and the puck sensor cannot sense obstacles
When a sensor detects its target object, the sensor is shaded red, otherwise it remains blue
Robot body
Left obstacle (wall or robot) sensor
Right obstacle (wall or robot) sensor
Puck sensor

## Slide 49: The gripper
The robot can grasp a sensed puck by creating a virtual spring between itself and the puck
Note that the sensor does not detect a grasped puck

## Slide 50: DEMO: PUCK COUNT
The main Waggle page has demo controllers that you can load:
  http://bots.cs.mun.ca/waggle/
Download grip_and_count.xml
Now go into the Pre-clustering level, click on “Choose File” and load it
Drag the robot around; As soon as it comes close to a puck it will grip it
Notice how it counts (at least up to 4) the number of pucks within sensor’s radius, but not including the puck held

## Slide 51: Blockly categories
We will now tour through the various blocks available
You can always get a helpful pop-up on any block by hovering your mouse above it:

## Slide 52: “Sensors” Category

## Slide 53
We’ll introduce these now
To be discussed later

## Slide 54
We know these blocks.
Note the ? at the end.
This signifies that the block produces a logical value: True or False.

## Slide 55
Indicates whether or not the centre of the robot is within the goal zone.

## Slide 56
Gives the number of red pucks in the sensor near the gripper.
The result is a number,
not a logical value.

## Slide 57
Logical value indicating whether a puck is currently held or not

## Slide 58: “ACTIONS” Category

## Slide 59
Sets forward and angular speeds (as we’ve seen)
Causes the controller to
execute for one time step
Displays the given text on top of the robot
After “Execute”, holds the last commanded speed for this number of milliseconds. Very useful for extended actions such as backing away from something or turning by a desired angle.
Note that while a speed is held, the controller is essentially frozen and cannot receive sensor data.
Activate / deactivate the gripper

## Slide 60
Remaining action blocks will be described later

## Slide 61: “LOGIC” Category

## Slide 62
The conditional block. Configure by
clicking star. Super important!
Relational operator. Compares the two number blocks and produces a logical value. By default tests numbers for equality, but this can be configured:

## Slide 63
Compares logical values. The two slots are for the logical blocks to compare. By default, produces True only if both values are True, but this can be configured:
and: True only if both inputs are True
or: True if one or both inputs are True

## Slide 64
Negates a logical value:
- True becomes False
- False becomes True
Always produces True (or False if selected)
(I’ve never used this... but you might like it)
If the “test” condition is true, returns the same logical value as the “if true” condition. Otherwise, returns the same logical value as
the “if false” condition. e.g. the following commands are equivalent:

## Slide 65: Boolean Expressions
You will sometimes need to form long expressions like this:
By right-clicking and selecting “External Inputs” you can re-format like so...
Applying ”External Inputs” to the sub-blocks we get to this form...

## Slide 66: “MATH” Category

## Slide 67
A fixed number
A fixed special number
Check number property (produces logical value)
Binary operation
Computes remainder after division
Constrains number within limits
Random integer within limits
Random number from 0 to 1
Unary operations on numbers

## Slide 68: Exercise #4: Don’t bump the pucks! 15 minutes
Start with the obstacle avoidance controller:
In the pre-clustering level create/load this controller; Increase the number of pucks to 100 and hit “Reset”
  The robot bumps into the pucks
Your goal is to create a controller that avoids the pucks, bumping into them as little as possible
Conditions:
1 robot

## Slide 69: Exercise #4: Don’t bump the pucks! 15 minutes
Modify the controller as follows:
Rearrange the following blocks to go into the empty slot:
The resulting controller won’t be perfect, but it should collide with fewer pucks
Conditions:
1 robot

## Slide 70: Exercise #4: Don’t bump the pucks! 15 minutes
Your controller will still probably collide with the occasional puck
Try rearranging your controller and tuning parameters to see if you can further reduce collisions
Conditions:
1 robot

## Slide 71: Exercise #5: FORAGING 20 minutes
Write a new controller that wanders about, looking for pucks. Upon encountering a puck it should pick it up. If a robot carrying a puck encounters the goal zone, it should drop it.
You will need the following components (along with others from the obstacle avoidance controller):
CHALLENGES:
  Robots may collide with pucks already in the goal zone. How can we handle this?
  If using fewer robots, they may not explore the environment fully. How can we handle this?
Conditions:
10 or more robots

## Slide 72: OBJECT CLUSTERING

## Slide 73: ANT CEMETARY CONSTRUCTION
Biologists have noticed many fascinating examples of social insects organizing their environments
e.g. Colonies of ants will cluster dead ants together, seemingly without any planning or supervision
A computational model was proposed to explain this behaviour:
  [Deneubourg, J. L., Goss, S., Franks, N., Sendova-Franks, A., Detrain, C., & Chrétien, L. (1991, February). The dynamics of collective sorting robot-like ants and ant-like robots. In Proceedings of the first international conference on simulation of adaptive behavior on From animals to animats(pp. 356-363).]

## Slide 74
Deneubourg et al’s model:
  Agents measure local object density by maintaining a short-term memory and counting the number of recent object appearances
  Agents walk randomly and pick-up or deposit objects as a probabilistic function of local object density
High
Medium
Low
Lower
Zero
Local object density (cartoon version)
Density | Pick-up Probability (if not carrying) | Deposit Probability (if carrying)
Low | High | Low
High | Low | High

## Slide 75
Not carrying
Carrying

## Slide 76
Experiments on the computational model closely match the results of biological experiments
But we have to be careful:
  Similarity of results does not necessarily imply similarity of method
Left:
Computer
Model
Right:
Biological
Experiment

## Slide 77: BECKERS ET AL
Beckers et al. wrote a paper detailing their experiments in swarm robotic clustering
  Beckers, R., Holland, O. E., & Deneubourg, J. L. (1994, July). From local actions to global tasks: Stigmergy and collective robotics. In Artificial life IV (Vol. 181, p. 189).
Unlike the [Deneubourg et al., 1990] model, the robot’s pick-up / deposit behaviour is implicit

## Slide 78
C-shaped gripper passively collects pucks
Infrared sensors detect obstacles (walls, other robots)
  Behaviour: Triggers random turn away from obstacle
Force sensor detects that gripper is pushing against three or more pucks
  Behaviour: Triggers backup, then a random turn, resulting in the pucks being left behind (i.e. deposited)
If no behaviour is triggered, the robot just moves straight

## Slide 79
Unlike Deneubourg et al. there is no explicit sensing of local object density
Yet when a high density area is encountered, the robot tends to further increase density by backing up and leaving its pucks behind
  POSITIVE FEEDBACK:
    Larger clusters are encountered more often, triggering further growth
  NEGATIVE FEEDBACK:
    When smaller clusters are encountered their pucks are taken away

## Slide 80: Clustering in waggle
The next task will be to consider a number of different possible sensor states and decide on reactions for each one
We’ll have to consider different numbers of pucks detected by the robot and decide whether they represent low or high density
For simplicity, lets say that a single puck is low-density and two or more pucks is high-density

## Slide 81
Fill in the blanks with the choices the robot should make; e.g.
Turn right
Turn right
Turn left
Turn left
Straight
Straight
Pick-up
Turn away
Deposit, then
turn away

## Slide 82
The answers are shown here:
Notes:
  To turn away by a fixed angle, use both “Set speeds” and “Hold speed”
  There are conditions not shown such as combinations of obstacles and pucks
Turn right
Turn right
Turn left
Turn left
Straight
Straight
Pick-up
Turn away
Deposit, then
turn away

## Slide 83: Exercise #6: OBJECT CLUSTERING 20 minutes
Create a new controller that has the appropriate response for all of the conditions just described
Beneath the simulation controls is a new plot called “Percentage Completion”
  Details:
    Computes the size of the largest cluster. Let this size be L
    PC = 100 * L / (number of pucks)
CHALLENGE:
  With 10 robots and 30 pucks, reach 60% completion within 200 seconds
Conditions:
Any number of robots and pucks

## Slide 84
Why does this work?
The other behaviours are necessary but only these two have a direct impact
Larger clusters attract more deposits than smaller clusters, leading to further growth and the gradual absorption of smaller clusters:
  Kazadi, S., Abdul-Khaliq, A., & Goodman, R. (2002). On the convergence of puck clustering systems. Robotics and Autonomous Systems, 38(2), 93-117.
Turn right
Turn right
Turn left
Turn left
Straight
Straight
Pick-up
Turn away
Deposit, then
turn away
POSITIVE FEEDBACK
NEGATIVE FEEDBACK

## Slide 85: Object Sorting

## Slide 86: OBJECT SORTING
Sorting objects is a natural extension of clustering
  Clustering: One object type
  Sorting: Two object types
It has potential applications in recycling, mining, and warehousing
Vardy, A., Vorobyev, G., & Banzhaf, W. (2014). Cache consensus: rapid object sorting by a robotic swarm. Swarm Intelligence, 8(1), 61-87.

## Slide 87: SORTING IN WAGGLE
Go to the main Waggle page (or just hit your browser’s back button):
  http://bots.cs.mun.ca/waggle/
Select the Sorting level. Note that there are now two different colours of pucks available: red and green
We will use the same sensor and action blocks as before, but will need to customize the “___ puck held” and “Number _____ pucks” blocks:

## Slide 88
When sorting two colors, we have more choices to make
Can you fill in the blanks?
Turn right

## Slide 89
Turn right
Turn left
Straight
Pick-up
Turn away
Deposit, then
turn away
Straight (breaking
up mixed cluster)

## Slide 90: Exercise #7: OBJECT SORTING 20 minutes
Create a new controller that has the appropriate response for all of the conditions just described
CHALLENGE:
  With 10 robots, 30 red pucks, and 30 green pucks, reach 50% completion within 200 seconds
Conditions:
Any number of robots and pucks

## Slide 91: Synchronization

## Slide 92: Firefly synchronization
Fireflies exhibit a remarkable behaviour where they flash in synchrony, apparently for reproduction
Since different species have different characteristic patterns, when the males flash appropriately the females can tell they have found an appropriate mate

## Slide 94: A simplified view
The patterns of flashing in fireflies can be complex
We take the simplified view of fireflies flashing in a single pulse
Exemplified by this video from Thailand:

## Slide 95: Why is this of interest to robotics?
Having a swarm of robots flash in synchrony has been proposed as a way to detect failures in other robots:
  That one’s not flashing right; It must be broken!
  Christensen, A. L., OGrady, R., & Dorigo, M. (2009). From fireflies to fault-tolerant swarms of robots. IEEE Transactions on Evolutionary Computation, 13(4), 754-766.
In general, we’re interested in how distributed agents can agree globally when each of them only has a very limited view of the world
  e.g. Agree on a set of locations for coloured pucks

## Slide 96: Flashing IN WAGGLE
Go to the main Waggle page (or just hit your browser’s back button):
  http://bots.cs.mun.ca/waggle/
Select the Fireflies level. There are no pucks and the robot has lost its puck sensor. But it has a large sensor that can detect flashes from other robots.
In “Sensors”: This gives the number of robots within the sensor’s area that were flashing during the last time step
In “Actions”: These illuminate and de-illuminate the robot

## Slide 97: Variables
All of our controllers so far have been completely reactive---behaviour depends only on the present input
But to make regular pulses of light the robots need to store something about the time since the last flash
Variables are a fundamental element in programming, but their use in Waggle is pretty limited:
  Only three variables available: variableA, variableB, and variableC
    For our purposes we will only need one
  They are integers, initialized to start at 0

## Slide 98: “Memory” Category
Set the variable to the given integer
Modify the variable by adding the given integer
Get the variable’s value as a number
Display the variable’s value on top of the robot (useful for debugging)

## Slide 99: Exercise #8: SIMPLE FLASHING 5 minutes
Create a controller like this:
  Add 1 to variableA
  If variableA = 10
    Activate flash
    Set variableA to 0
  Else
    Deactivate flash
  Execute
See what happens when you increase the number of robots
Play with “Timescale” slider to see things in slow motion
Incorporate
Note that robots are “born” at different times, and therefore will not be synchronized by default (although those with the same “birthday” will automatically synchronize)
Conditions:
Any number of robots (not trying to synchronize yet)

## Slide 100: Exercise #9: Synchronization 15 minutes
Start with the “fixed flasher” just created
If a neighbouring robot flashes, how should you respond so that you flash at the same time during the next cycle?
  Devise your own strategy based on this idea
Drag your robots around so that they form groups
You may wish to deselect “Show Sensors”
You may not get good performance unless the robots “mingle”
  Incorporate obstacle avoidance and keep the robots moving while they attempt to sync
Conditions:
Any number of robots

## Slide 101: Pheromones

## Slide 102: Pheromones: Insect communication
In many cases, insects deposit chemical signals called pheromones which can indicate something about a certain place or thing
The classic example of pheromone use is in ant foraging

## Slide 103: Finding the shortest path
When foraging for food, some ants leave behind pheromone trails on the ground:
  The pheromone is deposited by ants on their way back to the nest
  After the food source is exhausted the pheromone trail will dissipate
  Generally ants find the shortest path between food sources and the nest
  That’s a big deal! How can these tiny insects solve the problem of finding the shortest path?

## Slide 107
This is an example of positive feedback! The shorter branch has more pheromone deposited and therefore attracts the new ant. The new ant will also deposit more pheromone, amplifying the shorter branch even more!

## Slide 109
The pheromone deposited on the longer branch evaporates—an example of implicit negative feedback. If the ants forcibly removed the pheromone from that branch then we would say the negative feedback was explicit.

## Slide 110
It is important to note that the ants will usually reach a state of consensus, with the majority adopting one of the two branches. This is true even if both branches are the same length.

## Slide 111: PHEROMONES IN WAGGLE
Go to the main Waggle page (or just hit your browser’s back button):
  http://bots.cs.mun.ca/waggle/
Select the Pheromones level
The robot has a new layout of sensors:
Left/right obstacle sensors
Three pheromone / nest scent sensors
Puck sensor (enlarged)

## Slide 112
The “Select grid visibility” dropdown offers three choices:
No grid:
- White background just as before
Show Pheromone Grid:
Displays the quantity of pheromone:
  0: Black
  1: White
Appears black initially because no pheromone has been deposited
Show Nest Grid:
Displays the quantity of nest scent:
  0: Black
  1: White
Green pucks
(Food)
Nest

## Slide 113: Nest scent?
Once grabbing a puck (food) the robot needs to get it back to the nest
Real ants have a variety of navigation strategies:
  Visual homing by comparing the current image with one captured at the nest
  Learning their own visual path
  Path integration: Integrating velocity over time
We’ll simplify and assume they can somehow smell the nest over a wide area

## Slide 114
Each cell has a value in the range [0, 1] corresponding to its distance to the nest:
  0 (Black): Cell is at maximum distance to the nest
  1 (White): Cell is at the centre of the nest (distance 0)
So the nest scent grid forms a hill with the nest on top
This hill can be climbed by always moving in the direction of the highest sensor value

## Slide 115: New blocks
In the “Actions” Category:
  Emit this quantity of pheromones (10 by default)
  Value is divided by 10 internally
In the “Sensors” Category:
  Gives the quantity of either nest scent or pheromone underneath the left, ahead, or right sensor

## Slide 116: Exercise #10: HILL CLIMBING 15 minutes
Consider only nest scent, create a controller that moves towards the direction with the greatest nest scent
Once working, incorporate obstacle avoidance
CHALLENGE:
  The robot should be able to reach the nest from anywhere
Conditions:
1 robot

## Slide 117
Now experiment with this very simple controller by dragging the robot around:
Our goal is to develop a foraging controller which will leave pheromones behind whenever the robot has collected a green puck and is on its way home
Try this controller:
Like the one above, a robot using this controller needs the human user to drag it around. Try using it to collect all of the pucks in each pile:
  Notice how a new pile is generated

## Slide 118: Exercise #11: Pheromone-Aided foraging 30 minutes
Combine the following ideas to develop a controller that continually searches for green pucks using pheromones and returns with pucks to the nest:
  Controller from previous slide
  Hill climbing controller (ex. 10) for returning to the nest
  Obstacle avoidance
CHALLENGE:
  10 robots, 10 pucks: Once the controller is working, determine how long it takes to cycle through all three food piles
  Contrast this with the same controller which deposits no pheromones
Conditions:
Any number of robots

## Slide 119: Closing thoughts

## Slide 120: conclusions
We’ve approached swarm robotics through biologically-inspired examples
Waggle’s version of Blockly is quite limited---yet interesting and complex collective behaviour still emerges
Hopefully you’ve seen that swarm robotics is an engaging and accessible field!
Please let me know of any suggestions for improving Waggle or the experience of newcomers to swarm robotics:
  av@mun.ca
  bots.cs.mun.ca

## Slide 121: Waggle: Known issues / BUGS
”Slots” blocks not working
When the same controller is re-loaded, the load fails
Blockly area sizing
Arrow keys not the best choice for manual control
Pheromones: Robot gets trapped at nest while holding a puck (occurred with 10 robots, 10 pucks)

## Slide 122: WAGGLE ISSUES AT KAUST
1 random crash --- page became unresponsive
2 students found that when adding a block, the page would skip backwards to the main waggle page --- thus, eliminating their work
2 students found in the sorting application that the number of robots was decreasing! Number of pucks was also reducing.
1 student found unexpected behaviour due to the speeds being reset to 0; Workaround was to always have a “set speed” for all logical paths
Fireflies: Sensors staying red after flash from neighbour
Pheromones:
  Robot carrying puck could get stuck at goal
  Emited pheromones overwrite values in the pheromone grid instead of being added to them